## Slide 1: Assembly Language for x86 Processors 6th Edition
Chapter 1: Basic Concepts
Kip Irvine

## Slide 2: Chapter Overview
Welcome to Assembly Language
  X86 Processors
  MASM
Virtual Machine Concept
  Machines running other machines
Data Representation
  Bits and bytes
Boolean Operations
  AND, OR, NOT

## Slide 3: Welcome to Assembly Language
Some Good Questions to Ask
Assembly Language Applications

## Slide 4: Questions to Ask
Why am I learning Assembly Language?
  Oldest language; closest to HW
What background should I have?
What is an assembler?
  Translates assembly language into machine language
What hardware/software do I need?
What types of programs will I create?
  Console programs for 16-bit and 32-bit address mode
What do I get with this book?
What will I learn?
  Data rep; debugging; programming; HW manipulation

## Slide 5: Welcome to Assembly Language (cont)
How does assembly language (AL) relate to machine language?
  Machine language is numeric; AL is symbolic (almost)
How do C++ and Java relate to AL?
  One C++ or Java statement translates into many AL statements
Is AL portable?
  Usually NO
Why learn AL?
  Embedded programs, hardware interaction, OS, device drivers, game consoles

## Slide 6: Assembly Language Applications
Some representative types of applications:
  Business application for single platform
  Hardware device driver
  Business application for multiple platforms
  Embedded systems & computer games
(see next panel)

## Slide 7: Comparing ASM to High-Level Languages

## Slide 8: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 9: Virtual Machine Concept
Virtual Machines
Specific Machine Levels

## Slide 10: Virtual Machines
Tanenbaum: Virtual machine concept
Programming Language analogy:
  Each computer has a native machine language (language L0) that runs directly on its hardware
  A more human-friendly language is usually constructed above machine language, called Language L1
Programs written in L1 can run two different ways:
  Interpretation – L0 program interprets and executes L1 instructions one by one
  Translation – L1 program is completely translated into an L0 program, which then runs on the computer hardware

## Slide 11: Translating Languages
English: Display the sum of A times B plus C.
C++: cout << (A * B + C);
Assembly Language:
mov eax,A
mul B
add eax,C
call WriteInt
Intel Machine Language:
A1 00000000
F7 25 00000004
03 05 00000008
E8 00500000

## Slide 12: Specific Machine Levels
(descriptions of individual levels follow . . . )

## Slide 13: High-Level Language
Level 4
Application-oriented languages
  C++, Java, Pascal, Visual Basic . . .
Programs compile into assembly language (Level 3)

## Slide 14: Assembly Language
Level 3
Instruction mnemonics that have a one-to-one correspondence to machine language
Programs are translated into Instruction Set Architecture Level - machine language (Level 2)

## Slide 15: Instruction Set Architecture (ISA)
Level 2
Also known as conventional machine language
Executed by Level 1 (Digital Logic)

## Slide 16: Digital Logic
Level 1
CPU, constructed from digital logic gates
System bus
Memory
Implemented using bipolar transistors
next: Data Representation

## Slide 17: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 18: Data Representation
Binary Numbers
  Translating between binary and decimal
Binary Addition
Integer Storage Sizes
Hexadecimal Integers
  Translating between decimal and hexadecimal
  Hexadecimal subtraction
Signed Integers
  Binary subtraction
Character Storage

## Slide 19: Binary Numbers
Digits are 1 and 0
  1 = true
  0 = false
MSB – most significant bit
LSB – least significant bit
Bit numbering:

## Slide 20: Binary Numbers
Each digit (bit) is either 1 or 0
Each bit represents a power of 2:
Every binary number is a sum of powers of 2

## Slide 21: Translating Binary to Decimal
Weighted positional notation shows how to calculate the decimal value of each binary bit:
dec = (Dn-1  2n-1) + (Dn-2  2n-2) + ... + (D1  21) + (D0  20)
D = binary digit
binary 00001001 = decimal 9:
(1  23) + (1  20) = 9

## Slide 22: Translating Unsigned Decimal to Binary
Repeatedly divide the decimal integer by 2. Each remainder is a binary digit in the translated value:
37 = 100101

## Slide 23: Binary Addition
Starting with the LSB, add each pair of digits, include the carry if present.

## Slide 24: Integer Storage Sizes
What is the largest unsigned integer that may be stored in 20 bits?
Standard sizes:

## Slide 25: Hexadecimal Integers
Binary values are represented in hexadecimal.

## Slide 26: Translating Binary to Hexadecimal
Each hexadecimal digit corresponds to 4 binary bits.
Example: Translate the binary integer 000101101010011110010100 to hexadecimal:

## Slide 27: Converting Hexadecimal to Decimal
Multiply each digit by its corresponding power of 16:
  dec = (D3  163) + (D2  162) + (D1  161) + (D0  160)
Hex 1234 equals (1  163) + (2  162) + (3  161) + (4  160), or decimal 4,660.
Hex 3BA4 equals (3  163) + (11 * 162) + (10  161) + (4  160), or decimal 15,268.

## Slide 28: Powers of 16
Used when calculating hexadecimal values up to 8 digits long:

## Slide 29: Converting Decimal to Hexadecimal
decimal 422 = 1A6 hexadecimal

## Slide 30: Hexadecimal Addition
Divide the sum of two digits by the number base (16). The quotient becomes the carry value, and the remainder is the sum digit.
36 28 28 6A
42 45 58 4B
78 6D 80 B5
1
1
21 / 16 = 1, rem 5
Important skill: Programmers frequently add and subtract the addresses of variables and instructions.

## Slide 31: Hexadecimal Subtraction
When a borrow is required from the digit to the left, add 16 (decimal) to the current digit's value:
C6 75
A2 47
24 2E
-1
16 + 5 = 21
Practice: The address of var1 is 00400020. The address of the next variable after var1 is 0040006A. How many bytes are used by var1?

## Slide 32: Signed Integers
The highest bit indicates the sign. 1 = negative, 0 = positive
If the highest digit of a hexadecimal integer is > 7, the value is negative. Examples: 8A, C5, A2, 9D

## Slide 33: Forming the Two's Complement
Negative numbers are stored in two's complement notation
Represents the additive Inverse
Note that 00000001 + 11111111 = 00000000

## Slide 34: Binary Subtraction
When subtracting A – B, convert B to its two's complement
Add A to (–B)
0 0 0 0 1 1 0 0 0 0 0 0 1 1 0 0
– 0 0 0 0 0 0 1 1 1 1 1 1 1 1 0 1
0 0 0 0 1 0 0 1
Practice: Subtract 0101 from 1001.

## Slide 35: Learn How To Do the Following:
Form the two's complement of a hexadecimal integer
Convert signed binary to decimal
Convert signed decimal to binary
Convert signed decimal to hexadecimal
Convert signed hexadecimal to decimal

## Slide 36: Ranges of Signed Integers
The highest bit is reserved for the sign. This limits the range:
Practice: What is the largest positive value that may be stored in 20 bits?

## Slide 37: Character Storage
Character sets
  Standard ASCII (0 – 127)
  Extended ASCII (0 – 255)
  ANSI (0 – 255)
  Unicode (0 – 65,535)
Null-terminated String
  Array of characters followed by a null byte
Using the ASCII table
  back inside cover of book

## Slide 38: Numeric Data Representation
pure binary
  can be calculated directly
ASCII binary
  string of digits: "01010101"
ASCII decimal
  string of digits: "65"
ASCII hexadecimal
  string of digits: "9C"
next: Boolean Operations

## Slide 39: What's Next
Welcome to Assembly Language
Virtual Machine Concept
Data Representation
Boolean Operations

## Slide 40: Boolean Operations
NOT
AND
OR
Operator Precedence
Truth Tables

## Slide 41: Boolean Algebra
Based on symbolic logic, designed by George Boole
Boolean expressions created from:
  NOT, AND, OR

## Slide 42: NOT
Inverts (reverses) a boolean value
Truth table for Boolean NOT operator:
Digital gate diagram for NOT:

## Slide 43: AND
Truth table for Boolean AND operator:
Digital gate diagram for AND:

## Slide 44: OR
Truth table for Boolean OR operator:
Digital gate diagram for OR:

## Slide 45: Operator Precedence
Examples showing the order of operations:

## Slide 46: Truth Tables (1 of 3)
A Boolean function has one or more Boolean inputs, and returns a single Boolean output.
A truth table shows all the inputs and outputs of a Boolean function
Example: X  Y

## Slide 47: Truth Tables (2 of 3)
Example: X  Y

## Slide 48: Truth Tables (3 of 3)
Example: (Y  S)  (X  S)
Two-input multiplexer

## Slide 49: Summary
Assembly language helps you learn how software is constructed at the lowest levels
Assembly language has a one-to-one relationship with machine language
Each layer in a computer's architecture is an abstraction of a machine
  layers can be hardware or software
Boolean expressions are essential to the design of computer hardware and software

## Slide 50: Assembly Language for x86 Processors 6th Edition
Chapter 2: x86 Processor Architecture
Kip Irvine

## Slide 51: Chapter Overview
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 52: General Concepts
Basic microcomputer design
Instruction execution cycle
Reading from memory
How programs run

## Slide 53: Basic Microcomputer Design
clock synchronizes CPU operations
control unit (CU) coordinates sequence of execution steps
ALU performs arithmetic and bitwise processing

## Slide 54: Clock
synchronizes all CPU and BUS operations
machine (clock) cycle measures time of a single operation
clock is used to trigger events

## Slide 55: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 56: Instruction Execution Cycle
Fetch
Decode
Fetch operands
Execute
Store output
Instruction Execution Cycle

## Slide 57: Instruction Execution Cycle
Fetch – CU gets next instruction from the instruction queue and increments instruction pointer (IP)
Decode – CU determines the instruction’s function and the instruction’s input operands are sent to the ALU; signals are sent to ALU to tell it what to do
Fetch Operands – if operand is located in memory, CU issues a “read” to retrieve the data and put it in internal registers
Execute – ALU performs instruction and sends output to registers or memory
Store output operand – if operand is in memory, CU issues a “write” operation

## Slide 58: Reading from Memory (clock – GHz)
Multiple machine cycles are required when reading from memory, because it responds much more slowly than the CPU. The steps are:
  address placed on address bus
  Read Line (RD) set low
  CPU waits one cycle for memory to respond
  Read Line (RD) goes to 1, indicating that the data is on the data bus

## Slide 59: Cache Memory
High-speed expensive static RAM both inside and outside the CPU.
  Level-1 cache: inside the CPU
  Level-2 cache: outside the CPU
Cache hit: when data to be read is already in cache memory
Cache miss: when data to be read is not in cache memory.

## Slide 60: How a Program Runs

## Slide 61: Load and Execute Process
OS searches for program’s filename in disk directory, or in predetermined list (paths)
OS retrieves basic info about program from disk directory (file size, physical location)
OS determines free space in memory and loads the program; keeps data in descriptor file, and may adjust addresses within the program
OS begins execution of program. Now the program is called a process. OS assigns a process ID number.
OS tracks execution of program and responds to system resource requests from the program.

## Slide 62: Multitasking
OS can run multiple programs at the same time.
Multiple threads of execution within the same program.
Scheduler utility assigns a given amount of CPU time to each running program.
Rapid switching of tasks
  gives illusion that all programs are running at once
  the processor must support task switching.

## Slide 63: IA-32 Processor Architecture
Modes of operation
Basic execution environment
Floating-point unit
Intel Microprocessor history

## Slide 64: Modes of Operation
Protected mode
  native mode (Windows, Linux); programs cannot address outside area they are assigned
Real-address mode
  native MS-DOS; dangerous; direct access to HW
System management mode
  power management, system security, diagnostics
Virtual-8086 mode
  hybrid of Protected
  each program has its own 8086 computer

## Slide 65: Basic Execution Environment
Addressable memory
General-purpose registers
Index and base registers
Specialized register uses
Status flags
Floating-point, MMX, XMM registers

## Slide 66: Addressable Memory
Protected mode
  Linear up to about 4 GB
  32-bit address
  P6 processors can go to 64 GB
Real-address and Virtual-8086 modes
  1 MB space
  20-bit address

## Slide 67: General-Purpose Registers
Named storage locations inside the CPU, optimized for speed.

## Slide 68: The alphabet
A = Accumulator P = Pointer
B = Base X = Register
C = Counter or Code
D = Data
E = Extended
F = Flag
I = Index or Instruction
H = High
L = Low
S = Segment or Stack

## Slide 69: Accessing Parts of Registers
Use 8-bit name, 16-bit name, or 32-bit name
Applies to EAX, EBX, ECX, and EDX

## Slide 70: Index and Base Registers
Some registers have only a 16-bit name for their lower half:

## Slide 71: Some Specialized Register Uses (1 of 2)
General-Purpose
  EAX – accumulator
  ECX – loop counter
  ESP – stack pointer
  ESI, EDI – index registers
  EBP – extended frame pointer (stack)
Segment
  CS – code segment
  DS – data segment
  SS – stack segment
  ES, FS, GS - additional segments

## Slide 72: Some Specialized Register Uses (2 of 2)
EIP – instruction pointer
EFLAGS
  status and control flags
  each flag is a single binary bit

## Slide 73: Status Flags
Carry -CF
  unsigned arithmetic out of range
Overflow - OF
  signed arithmetic out of range
Sign - SF
  result is negative
Zero - ZF
  result is zero
Auxiliary Carry - AF
  carry from bit 3 to bit 4
Parity - PF
  sum of 1 bits is an even number
Trap – TF
  Causes processor to execute in single steps
Interrupt – IF
  Disable external interrupts
Direction – DF
  Used in string operations

## Slide 74: Flag Register Bits
 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00
 |  |  |  | O | D | I | T | S | Z |  | A |  | P |  | C

## Slide 75: Floating-Point, MMX, XMM Registers
MM = Multimedia
Eight 80-bit floating-point data registers
  ST(0), ST(1), . . . , ST(7)
  arranged in a stack
  used for all floating-point arithmetic
Eight 64-bit MMX registers
Eight 128-bit XMM registers for single-instruction multiple-data (SIMD) operations

## Slide 76: Intel Microprocessor History
Intel 8086, 80286
IA-32 processor family
P6 processor family
CISC and RISC

## Slide 77: Early Intel Microprocessors
Intel 8080
  64K addressable RAM
  8-bit registers
  CP/M operating system
  S-100 BUS architecture
  8-inch floppy disks!
Intel 8086/8088
  IBM-PC Used 8088
  1 MB addressable RAM
  16-bit registers
  16-bit data bus (8-bit for 8088)
  separate floating-point unit (8087)

## Slide 78: The IBM-AT
Intel 80286
  16 MB addressable RAM
  Protected memory
  several times faster than 8086
  introduced IDE bus architecture
  IDE = Integrated Drive Electronics
  80287 floating point unit

## Slide 79: Intel IA-32 Family
Intel386
  4 GB addressable RAM, 32-bit registers, paging (virtual memory)
Intel486
  instruction pipelining
Pentium
  superscalar, 32-bit address bus, 64-bit internal data path

## Slide 80: 64-bit Processors
Intel64
  64-bit linear address space
  Intel: Pentium Extreme, Xeon, Celeron D, Pendium D, Core 2, and Core i7
IA-32e Mode
  Compatibility mode for legacy 16- and 32-bit applications
  64-bit Mode uses 64-bit addresses and operands

## Slide 81: Intel Technologies
HyperThreading technology
  two tasks execute on a single processor at the same time
Dual Core processing
  multiple processor cores in the same IC package
  each processor has its own resources and communication path with the bus

## Slide 82: Intel Processor Families
Currently Used:
Pentium & Celeron – dual core
Core 2 Duo - 2 processor cores
Core 2 Quad - 4 processor cores
Core i7 – 4 processor cores

## Slide 83: CISC and RISC
CISC – complex instruction set
  large instruction set
  high-level operations
  requires microcode interpreter
  examples: Intel 80x86 family
RISC – reduced instruction set
  simple, atomic instructions
  small instruction set
  directly executed by hardware
  examples:
    ARM (Advanced RISC Machines)
    DEC Alpha (now Compaq)

## Slide 84: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 85: IA-32 Memory Management
Real-address mode
Calculating linear addresses
Protected mode
Multi-segment model
Paging

## Slide 86: Real-Address mode
1 MB RAM maximum addressable
Application programs can access any area of memory
Single tasking
Supported by MS-DOS operating system

## Slide 87: Segmented Memory
Segmented memory addressing: absolute (linear) address is a combination of a 16-bit segment value added to a 16-bit offset
linear addresses
one segment

## Slide 88: Calculating Linear Addresses
Given a segment address, multiply it by 16 (add a hexadecimal zero), and add it to the offset
Example: convert 08F1:0100 to a linear address
Adjusted Segment value: 0 8 F 1 0
Add the offset: 0 1 0 0
Linear address: 0 9 0 1 0

## Slide 89: Your turn . . .
What linear address corresponds to the segment/offset address 028F:0030?
028F0 + 0030 = 02920
Always use hexadecimal notation for addresses.

## Slide 90: Your turn . . .
What segment addresses correspond to the linear address 28F30h?
Many different segment-offset addresses can produce the linear address 28F30h. For example:
28F0:0030, 28F3:0000, 28B0:0430, . . .

## Slide 91: Protected Mode (1 of 2)
4 GB addressable RAM
  (00000000 to FFFFFFFFh)
Each program assigned a memory partition which is protected from other programs
Designed for multitasking
Supported by Linux & MS-Windows

## Slide 92: Protected mode (2 of 2)
Segment descriptor tables
Program structure
  code, data, and stack areas
  CS, DS, SS segment descriptors
  global descriptor table (GDT)
MASM Programs use the Microsoft flat memory model

## Slide 93: Flat Segment Model
Single global descriptor table (GDT).
All segments mapped to entire 32-bit address space

## Slide 94: Multi-Segment Model
Each program has a local descriptor table (LDT)
  holds descriptor for each segment used by the program

## Slide 95: Paging
Supported directly by the CPU
Divides each segment into 4096-byte blocks called pages
Sum of all programs can be larger than physical memory
Part of running program is in memory, part is on disk
Virtual memory manager (VMM) – OS utility that manages the loading and unloading of pages
Page fault – issued by CPU when a page must be loaded from disk

## Slide 96: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 97: Components of an IA-32 Microcomputer
Motherboard
Video output
Memory
Input-output ports

## Slide 98: Motherboard
CPU socket
External cache memory slots
Main memory slots
BIOS (basic input/output system) chips
Sound synthesizer chip (optional)
Video controller chip (optional)
IDE, parallel, serial, USB, video, keyboard, joystick, network, and mouse connectors
PCI bus connectors (expansion cards)

## Slide 99: Intel D850MD Motherboard
dynamic RAM
Pentium 4 socket
Speaker
IDE drive connectors
mouse, keyboard, parallel, serial, and USB connectors
AGP slot
Battery
Video
Power connector
memory controller hub
Diskette connector
PCI slots
I/O Controller
Firmware hub
Audio chip
Source: Intel® Desktop Board D850MD/D850MV Technical Product Specification

## Slide 100: Intel 965 Express Chipset

## Slide 101: Video Output
Video controller
  on motherboard, or on expansion card
  AGP (accelerated graphics port technology)*
Video memory (VRAM)
Video CRT Display
  uses raster scanning
  horizontal retrace
  vertical retrace
Direct digital LCD monitors
  no raster scanning required
* This link may change over time.

## Slide 102: Sample Video Controller (ATI Corp.)
  128-bit 3D graphics performance powered by RAGE™ 128 PRO
  3D graphics performance
  Intelligent TV-Tuner with Digital VCR
  TV-ON-DEMAND™
  Interactive Program Guide
  Still image and MPEG-2 motion video capture
  Video editing
  Hardware DVD video playback
  Video output to TV or VCR

## Slide 103: Memory
ROM
  read-only memory
EPROM
  erasable programmable read-only memory
Dynamic RAM (DRAM)
  inexpensive; must be refreshed constantly
Static RAM (SRAM)
  expensive; used for cache memory; no refresh required
Video RAM (VRAM)
  dual ported; optimized for constant video refresh
CMOS RAM
  complimentary metal-oxide semiconductor
  system setup information
See: Intel platform memory (Intel technology brief: link address may change)

## Slide 104: Input-Output Ports
USB (universal serial bus)
  intelligent high-speed connection to devices
  up to 12 megabits/second
  USB hub connects multiple devices
  enumeration: computer queries devices
  supports hot connections
Parallel
  short cable, high speed
  common for printers
  bidirectional, parallel data transfer
  Intel 8255 controller chip

## Slide 105: Input-Output Ports (cont)
Serial
  RS-232 serial port
  one bit at a time
  uses long cables and modems
  16550 UART (universal asynchronous receiver transmitter)
  programmable in assembly language

## Slide 106: Device Interfaces
ATA host adapters
  intelligent drive electronics (hard drive, CDROM)
SATA (Serial ATA)
  inexpensive, fast, bidirectional
FireWire
  high speed (800 MB/sec), many devices at once
Bluetooth
  small amounts of data, short distances, low power usage
Wi-Fi (wireless Ethernet)
  IEEE 802.11 standard, faster than Bluetooth

## Slide 107: What's Next
General Concepts
IA-32 Processor Architecture
IA-32 Memory Management
Components of an IA-32 Microcomputer
Input-Output System

## Slide 108: Levels of Input-Output
Level 3: High-level language function
  examples: C++, Java
  portable, convenient, not always the fastest
Level 2: Operating system
  Application Programming Interface (API)
  extended capabilities, lots of details to master
Level 1: BIOS
  drivers that communicate directly with devices
  OS security may prevent application-level code from working at this level

## Slide 109: Displaying a String of Characters
When a HLL program displays a string of characters, the following steps take place:

## Slide 110: Programming levels
Assembly language programs can perform input-output at each of the following levels:

## Slide 111: Summary
Central Processing Unit (CPU)
Arithmetic Logic Unit (ALU)
Instruction execution cycle
Multitasking
Floating Point Unit (FPU)
Complex Instruction Set
Real mode and Protected mode
Motherboard components
Memory types
Input/Output and access levels